## Slide 1
CTC Panel Configuration
&
Technology Update

## Slide 2
Video #9
Video #10

## Slide 4
NodeMCD 32-S Controller
LocoNet Interface Board
Touch Button Multiplexer
LED Chain Connection

## Slide 9
Table of content Min/Sec
Introduction to Configuration 0:51
CTC Panel Basic Config Demo 3:15
LocoNet to MQTT Gateway Message Update 8:45
Touch Button Auto Configuration 11:20
Websocket Communication 14:00
Summary 16:16

## Slide 10: Capabilities
LED’s: Basically not limited, for sure more than what you can physically place on the CTC panel
Buttons: 64 input lines to be used as touch or digital buttons, or analog inputs
LocoNet Commands: Send Switch commands, receive Switch Position and Block Detector Messages from the LocoNet network
MQTT Commands (if connected to Wifi and MQTT broker): Same as LocoNet, plus send and receive button and status information between CTC panels for coordination and remote control
The Yellow Box can act as LocoNet to MQTT Gateway (if connected to Wifi and MQTT broker)
Wifi: Supports Access Point or Station Mode
Support of ABS and CTC control models for train movements
Supports true two button operation for selection of routes
Configuration using a web browser on a PC or Mobile Phone with Wizard support

## Slide 12
?

## Slide 14
Example Router Configuration Page
Yours may look different, but has same content

## Slide 16: Gateway Message Flow with Response
Slot Data Request 0xBB
Read Slot Data 0xE7
LocoNet Response Time in μSecs

## Slide 17
MUX Input | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Open Value | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Cable connected | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15
Touch Value | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
Multiplexed Touch Input Measurements on GPIO #13*
* Other tested pins show almost identical results. Tested with pins 12, 13, 14, 27
Conclusions:
Very stable and repetitive behavior after MUX
Difference between touched and untouched is not much, but sufficient for reliable detection
Best results when measuring in bursts of 5 measurements and averaging the results. So far I have not seen any false positives or false negatives

## Slide 18
MUX Input | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Open Value | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Cable connected | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15
Touch Value | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
Touch Value 2** | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 2 | 2 | 1
Multiplexed Touch Input Measurements on GPIO #13*
* Other tested pins show almost identical results. Tested with pins 12, 13, 14, 27
** Performing a TouchRead operation while pin is connected to a voltage source between GND and Vcc (0 – 3.3V)
Conclusions:
Very stable and repetitive behavior after MUX
Difference between touched and untouched is not much, but sufficient for reliable detection
Best results when measuring in bursts of 5 measurements and averaging the results. So far I have not seen any false positives or false negatives
When an analog signal is connected, the touchRead value is always very low, typically 1 or 2, independent of the signal voltage

## Slide 19
Calculate average value for 5 read ops
Calculate rolling average
Repeat numRead=5 times for stabilized read result

## Slide 20
Treat data as touch input if touch value is more than 5
Otherwise evaluate analog data value. If within 1% of upper and lower limits, interpret as digital input, otherwise send analog value event

## Slide 21
16 Input Analog MUX
16 Input Lines

## Slide 22
Push Button (normally open)
Pullup Resistor to Vcc
GND Wire
Vcc Wire
Potentiometer
Input Wire
GND Wire

## Slide 30: Summary
The Yellow Box can be configured to a wide variety of different requirements. This makes configuration very complex and a display based user dialog is almost a must
Since almost everyone has one, it makes sense to use a smart phone and a wireless connection to support device configuration
How this can work we have seen so far with the example of the general device configuration dialog
Another approach to reduce configuration complexity is making the devices smarter. Self configuring input lines is just one example
A good configuration screen also should use some Wizard technology to do the work for the user.
The use of websockets allows for continuous bidirectional communication between the device and the web browser.

## Slide 31
if (watching_this(video) == (useful || interesting))
{
please_click_like();
}

## Slide 32
Additional Materials on Github: https://github.com/tanner87661/IoTT-Video11
Websockets Intro: https://www.html5rocks.com/en/tutorials/websockets/basics/
Websockets Wiki: https://en.wikipedia.org/wiki/WebSocket
Layout Intro Sequence Outdoor Layout: Beat Deola, Switzerland​
Indoor Layout Videos: Hendersonville, NC Train Depot https://www.avmrc.com/​